# Lab #2 – Introduction to Excel and References
Created on: 31 July 2019
By: Samuel Bechara, PhD
## Technical Objectives
- Calculate with cell referencing in Microsoft Excel
- Utilize functions built in to Excel
## Sweet Reference, Dude
You must determine if the three balls your TA/LA hands out will sink or float. To do this, you will be calculating the average specific gravity (note these are not homogeneous so this is not a calculation of true specific gravity) of the three balls in two different ways: by hand and using cell referencing in Excel. You will measure the diameter of each ball in inches, convert to radius in cm, and use the equation given below to calculate volume in cm3. You can then calculate density in g/cm3 and specific gravity (density of object divided by the density of water, 1 g/cm3).
V = {4}over{3} %pi R^3
First, calculate the specific gravity of the softball (mass of 200 g) by hand. Then, do the same calculation using referencing in Excel using the worksheet titled “Problem A”. Next, determine the specific gravity of the rubber ball (mass of 100 g) and of the tennis ball (mass of 60 g) by whichever method you choose. Which method is faster to repeat the calculation? Which balls will sink or float?
### Lunar Table
You are on the moon conducting a repeat of David Scott’s experiment where he dropped a feather and a hammer. First, you will estimate the potential energy across a range of objects and heights. Use the worksheet template “Problem B” to calculate the average, maximum, and minimum potential energy values for ten objects raised to twenty different heights each as given in the worksheet. Assume the acceleration due to gravity on the moon is 1.60 m/s2.

### Totally Turbulent
The energy required to transport ethanol through piping is an important environmental concern. The type of flow, as characterized with the Reynold’s number, influences the required energy to transport ethanol through this piping. Recall the equation for Reynold’s number, which is a dimensionless number that characterizes fluid flow within a channel. Given the diameter, D and velocity, v, data given in the Excel worksheet titled “Problem C”, calculate the Reynold’s number for each set of measurements. All data provided are for ethanol, which has a viscosity of 0.0011 kg/m-s and a density of 0.78 g/cm3.
{R e} = { D %rho v }over{ %mu }
Use the COUNTIF function to determine how many of the diameter-velocity pairs are laminar (Re<2000), transitional (2000<Re<4000), or turbulent (Re>4000). Be aware of units and unit conversions.